## Slide 1: The ambiguity function with applications
Ellory Freneau

## Slide 2: High-level Radar System
An adversary is at location X.
The adversary is moving with signed velocity .
The type of pulse effects resolution and different detection properties.
        - Distance (m)
        - Speed of light (m/s)
        - Two-way time delay (s)
        - Doppler shift (Hz)
        - Source frequency (Hz)
        - Velocity of source (m/s)
        - Velocity of receiver (m/s)

## Slide 3
Question
How distinguishable are doppler shifted and delayed versions of a signal from each other?

## Slide 4: The Received Pulse
Received waveform is effected by Doppler shift and time delay.
Pulses are detected using a matched filter (equivalent to correlation).
(1)
(2)
(3)

## Slide 5: The Ambiguity Function
The Ambiguity function is a measure similarity between a pulse and delayed and/or frequency shifted versions of itself.
or
The Ambiguity function is equivalent to autocorrelation in the slice.
Ideal ambiguity is an impulse at X(0,0) and 0 elsewhere.

## Slide 6: Discrete computation of Ambiguity
Integral turns to summation over the N elements of the input sequence.
Frequency shift kernel is a sequence of equal size.
Time shift is done N-times and is circular.

## Slide 7: Fast Implementation
The above is done N more times, therefore…
Complexity:
Steps: [1] complex conjugate. [2] circular shift by K. [3] element-wise multiply. [4] N-point IFFT. [5] Repeat for each K.

## Slide 8: Applications to relevant sequences

## Slide 9: Square Pulse (MATLAB)
Ambiguity function of a square pulse (40 samples) from MATLAB.

## Slide 10: Square Pulse
Ambiguity function of a square pulse (40 samples).

## Slide 11: Colormap and Contour
Quadratic chirp ambiguity represented 3 ways.

## Slide 12: Slicing in time or frequency
Doppler and delay slice plots for a quadratic chirp.

## Slide 13: Barker-13 Sequence
Minimum correlation sidelobes (-22.3 dB)
Longest Barker sequence.

## Slide 14: Maximum Length Sequence (MLS)
Longest non-repeated sequence for a finite shift register.
Cyclically repeating every samples.
4-Bit Galois Field:

## Slide 15: Chirp (Linear)
: frequency range over duration.

## Slide 16: Zadoff-Chu Sequence
Estimate a fading channel (multipath).
Used in LTE cellular for synch and coherent combining.
Circular shift produces an orthogonal signal.

## Slide 17: Damped Sinusoid
Short-time single tone (simple wavelet)

## Slide 18: Additive White Gaussian Noise
By definition…
Where is the variance of the process.

## Slide 19: PRN Code in GPS
C/A Code in GPS is 1023-bit sequence (37 unique codes).
Each GPS satellite has its own orthogonal code (31 in use as of 2020).

## Slide 20: Project Code
https://github.com/efreneau/Ambiguity-Function
Some plots: https://raw.githack.com/efreneau/Ambiguity-Function/master/Plots.html

## Slide 21: Sources
https://upload.wikimedia.org/wikipedia/commons/3/37/Radar_animation.gif
https://en.wikipedia.org/wiki/Doppler_effect#/media/File:Dopplereffectsourcemovingrightatmach0.7.gif
https://en.wikipedia.org/wiki/Chirp#/media/File:Linear-chirp.svg
https://en.wikipedia.org/wiki/Maximum_length_sequence#/media/File:MLS_shiftregisters_L4.png
https://i.stack.imgur.com/UOQnn.png